Design Considerations
- DUE TO:
  - Hub clock frequency >> link bandwidth
  - Data center access expensive
- MUST:
  - Capacity of hub memory is most important parameter
- HOW:
  - Use almost all possible M3 and M2

---
Design Considerations
- DUE TO:
  - Maximize throughput while minimizing latency
- SHOULD:
  - Memory subsystem must be designed intelligently
- HOW:
  - Interleaving memory banks

---
Design Considerations
- DUE TO:
  - Eviction and replacement of data
  - Finite memory
- SHOULD:
  - Data stored flexibly will increase performance
- HOW:
  - Non-contiguous memory access

---
Design Considerations
- DUE TO:
  - Expensive data center (time & money)
- MUST:
  - Minimize data center access
- HOW:
  - Use efficient and flexible caching policy

---
Design Considerations
Summary
- MUST:
  - Large capacity
  - Minimize data center accesses
- SHOULD:
  - Efficient memory system
  - Flexible memory access
- HOW:
  - M2 & M3 banks
  - Interleaving memory
  - Non-contiguous memory access
  - Efficient cache algorithm

---
How to manage such a system?
- Use an M1 as virtual memory!
- CONS:
  - $50
- PROS:
  - Fast access times
  - M3 & M2 address space mapping
  - Valid data mapping for improved performance
  - Provides platform for increased flexibility (word storage, cache implementation)

---
Why not just use a large amount of cheaper memory?
- Scalable!
- As link bandwidths increase, performance will increase
- Interleaved memory and memory map allows for efficient and fast caching

---
Requirements
Assumptions
3 connected devices
Send data of size TS
Receive data of size TS
TS = 128/512/1024 bytes
1 Satellite link
Optimize for:
Latency (user wait time)
Communication cost ($/min)
Unit cost (memory price)
Internal communication:
16-bit data bus
1 cycle between memories
16-bit buffers
1 cycle latency
Satellite communication:
32-bit command
Hub to satellite latency:
100 cycles
Data center to satellite latency:
50 cycles
1200bits/s to/from S/DC
5 bits of data are tag
Data with same tag has same TS
No SEND to same tag twice
Satellite
Data
Center
1200b/s
1200b/s
Hub
5.5Mb/s
Device
2
Device
1
Device
3

---
M1
Specs
$50
Latency: 1 cycle
256 bytes (2x128)
Design
Qty: 1 (2x128)
Cost: $50
M2
Specs
$10
Latency: 8 cycles
512 bytes (2x256)
Design
Qty: 4 (8x256)
Cost: $40
M3
Specs
$3
Latency: 15 cycles
1024 bytes (2x512)
Design
Qty: 8 (16x512)
Cost: $24
2 bytes
0
.
.
.
M1
127
8 bytes
0
.
.
.
M3
M2
M2
M3
M2
M2
255
16 bytes
0
.
.
.
M3
M3
M3
M3
M3
M3
M3
M3
M3
M3
M3
M3
511

---
Each memory module is designed to be dumb.
They only have two operations: Read and Write.
The memory controller tells the memory which row
to write to and what data to write.
It is the memory controller's responsibility to ensure
that no read or write operations occur while a read
or write is already taking place (by checking the
mem_lock variable).
Write
4 parallel banks
Memory aligned in increments
of 16 rows (e.g., 0x0, 0x16, 0x32)
TS=128: 16 rows
TS=512: 64 rows
TS=1024: 128 rows
M2
Data In
Data Out
Read
Row
8 parallel banks
Memory aligned in increments
of 8 rows (e.g., 0x0, 0x8, 0x16)
TS=128: 8 rows
TS=512: 32 rows
TS=1024: 64 rows
Write
M3
Data In
Data Out
Read
Row

---
M1
2x128
M2
8x256
M3
16x512
Device
1
Satellite
Link
Device
2
Device
3

---
Cache Controller Memory
One M1 memory module is used as the memory for the
cache controller to act as a virtual address space for the M2
and M3 memories. Each line corresponds to a “block” (128 lines)
in the respective memories.
M3 Memory Map:	0x00 – 0x3F (64 lines)
M2 Memory Map:	0x40 – 0x4F (16 lines)
[15:14]	type	00 – Word	(TS = 128) (1 block)
01 – Quad	(TS = 512) (4 blocks)
10 – Long	(TS = 1024) (8 blocks)
11 – Invalid
[13:9]	tag	Tag of data
[8]	rsvd	Always 0
[7:1]	next	Row in cache controller containing
next segment (no next = 1111111b)
[0]	rsvd	Always 0
0xFE = Invalid Line
0x00
.
.
.
0x4F
type
type
tag
tag
tag
tag
tag
0
next
next
next
next
next
next
next
0
bit 0
bit 15

---
Cache Controller Memory
The rest of the M1 memory is used to track which of the blocks of memory
have empty spots.
A 0 in a bit means that the corresponding block is empty.
A 1 in a bit means that the corresponding block contains valid data.
M3 Valid Map:	0x50 – 0x53
M2 Valid Map:	0x54
0x50
type
block
0
type
block
1
addr
block
2
addr
block
3
addr
block
4
addr
block
5
addr
block
6
addr
block
7
type
block
8
type
block
9
addr
block
10
addr
block
11
addr
block
12
addr
block
13
addr
block
14
addr
block
15
0x51
type
block
16
type
block
17
addr
block
18
addr
block
19
addr
block
20
addr
block
21
addr
block
22
addr
block
23
type
block
24
type
block
25
addr
block
26
addr
block
27
addr
block
28
addr
block
29
addr
block
30
addr
block
31
M3 Map
0x52
type
block
32
type
block
33
addr
block
34
addr
block
35
addr
block
36
addr
block
37
addr
block
38
addr
block
39
type
block
40
type
block
41
addr
block
42
addr
block
43
addr
block
44
addr
block
45
addr
block
46
addr
block
47
0x53
type
block
48
type
block
49
addr
block
50
addr
block
51
addr
block
52
addr
block
53
addr
block
54
addr
block
55
type
block
56
type
block
57
addr
block
58
addr
block
59
addr
block
60
addr
block
61
addr
block
62
addr
block
63
0x54
type
block
64
type
block
65
addr
block
66
addr
block
67
addr
block
68
addr
block
69
addr
block
70
addr
block
71
type
block
72
type
block
73
addr
block
74
addr
block
75
addr
block
76
addr
block
77
addr
block
78
addr
block
79
M2 Map

---
Memory Map
The M2 and M3 memories are mapped into the M1 memory as a series of
blocks. Each block is 128 bytes, so that any TS can be stored anywhere in
chunks.
TS=128	– 1 block
TS=512	– 4 blocks
TS=1024	– 8 blocks
The M1 memory map keeps track of where the data of a certain tag is located
throughout the memory space through the next field, which contains the M1
row containing the next block. The cache controller goes to the lowest M1
address and follows the trail of next fields until it reaches a next field of 0x7E,
indicating that there is no next.

---
SEND
Enough blocks
to hold TS?
No
Yes
Find blocks
of same TS
Write data to
memory
Find blocks
with lowest tag
Update
memory map
Send data to
data center
Overwrite old
blocks with new
data
Update
memory map

---
REQUEST
Data in cache?
No
Yes
Find blocks
of same TS
Return data
to device
Find a
with lowest tag
Get data from
data center
Overwrite old
blocks with new
data
Update
memory map
Return data
to device

---
M3
0	1	2	3	4	5	6	7	Bytes Trsfrd
t = 0	1	2	3	4	5	6	7	0
16	17	18	19	20	21	22	23	16
32	33	34	35	36	37	38	39	32
48	49	50	51	52	53	54	55	48
64	65	66	67	68	69	70	71	64
80	81	82	83	84	85	86	87	80
96	97	98	99	100	101	102	103	96
112	113	114	115	116	117	118	119	112
127	128	129	130	131	132	133	134	128
Total Time: 134 cycles

---
M2
Bank 0	Bank1	Bank2	Bank3	Bytes Trsfrd
t = 0	1	2	3	0
9	10	11	12	8
18	19	20	21	16
27	28	29	30	24
36	37	38	39	32
45	46	47	48	40
54	55	56	57	48
63	64	65	66	56
72	73	74	75	64
81	82	83	84	72
90	91	92	93	80
99	100	101	102	88
108	109	110	111	96
117	118	119	120	104
126	127	128	129	112
135	136	137	138	120
143	144	145	146	128
Total Time: 146 cycles